## Slide 1
Microprocessor Architecture ECE4375/5375
Dr. Argenis Bilbao
Spring 2026

## Slide 2: Presentation Outline
CPU Architectures
Computer Buses

## Slide 3: The 8088 Computer Architecture
All devices are connected to the CPU bus (8-bit bus)
Advantages
Simplicity
Disadvantages
High amounts of congestion
CPU is completely halted if two devices are communicating between each other (DMA, CPU with no cache)
IBM 8086 and 286 used the same topology but with a 16-bit bus.
ISA Bus was predominant

## Slide 4: A More Complicated System
Starting with the original Pentium, a “north bridge was used between the CPU bus and the rest of the buses in the system
32-bit CPU bus from 486 to original Pentium
Advantages
Allowed for multiple buses to exist within a computer system
These busses could be using DMA to communicate between devices.
Theoretically unlimited number of CPUs in the system
Disadvantages
Obviously more complicated system
Memory no longer connected directly to CPU
Congestion in the CPU bus

## Slide 5: The PCI Bus
32-bit/64-bit address and data bus
Advantages over ISA bus
Increased bandwidth from 16Mb/s to 1067Mb/s for base version to 8.5 Gb/s for PCI-X 133 MHz
Platform independent bus (also used in Apple systems and others)
Disadvantages
Still uses a shared bus so only two devices can communicate at the same time if on the same bus

## Slide 6: The PCI Bus

## Slide 7: The PCI Bus Pins
http://www.interfacebus.com/Design_PCI_Pinout.html

## Slide 8: An Even More Complicated System
64-bit CPU bus from Pentium 4 to present
Still was plagued by the same “bottlenecking” issue as machines before it
Manufacturers tried to remedy the problem by increasing FSB speed and increasing the number of memory channels in server machines
Enough is enough!

## Slide 9: An Even More Complicated System

## Slide 10: Systems We Enjoy Today
4th Generation Xeon Scalable machine
No north bridge!
Memory directly attached to the CPU (internal memory controller)
Ultra path interconnect (UPI) between CPUs to allow other CPUs to access the memory
UPI also used to keep cache coherency between CPUs

## Slide 11: Systems We Enjoy Today

## Slide 12: PCIe Bus
Version 1.x: 2.5 GT/s
x1: 250 MB/s
x16: 4 GB/s
Version 2.x: 5 GT/s
x1: 500 MB/s
x16: 8 GB/s
Version 3.x: 8 GT/s
x1: 985 MB/s
x16: 15.75 GB/s
Version 4.0: 16 GT/s
x1: 1.97 GB/s
x16: 31.5 GB/s
Version 5.0: 32 GT/s
x1: 3.94 GB/s
x16: 63 GB/s
Version 6.0: 64 GT/s
x1: 7.56 GB/s
x16: 121 GB/s
Version 7.0: 128 GT/s
x1: 15.13 GB/s
x16: 242 GB/s

## Slide 13: PCIe 1x Slot Pins
Pin | Side B Connector |  | Side A Connector | 
# | Name | Description | Name | Description
1 | +12v | +12 volt power | PRSNT#1 | Hot plug presence detect
2 | +12v | +12 volt power | +12v | +12 volt power
3 | +12v | +12 volt power | +12v | +12 volt power
4 | GND | Ground | GND | Ground
5 | SMCLK | SMBus clock | JTAG2 | TCK
6 | SMDAT | SMBus data | JTAG3 | TDI
7 | GND | Ground | JTAG4 | TDO
8 | +3.3v | +3.3 volt power | JTAG5 | TMS
9 | JTAG1 | +TRST# | +3.3v | +3.3 volt power
10 | 3.3Vaux | 3.3v volt power | +3.3v | +3.3 volt power
11 | WAKE# | Link Reactivation | PERST# | PCI-Express Reset signal
Mechanical Key |  |  |  | 
12 | RSVD | Reserved | GND | Ground
13 | GND | Ground | REFCLK+ | Reference Clock Differential pair
14 | HSOp(0) | Transmitter Lane 0, Differential pair | REFCLK- | 
15 | HSOn(0) |  | GND | Ground
16 | GND | Ground | HSIp(0) | Receiver Lane 0, Differential pair
17 | PRSNT#2 | Hotplug detect | HSIn(0) | 
18 | GND | Ground | GND | Ground

## Slide 14: Sources
http://www.eecs.harvard.edu/cs146-246/
Assigned Textbook
https://www.supermicro.com/